## Slide 1: Internet of Everything Module 3. Principles of Connected Devices and Protocols in IoT
IT – BE – IoE
Prof. Nita Patil
Assistant Professor
Dept. of Electronics & Computer Science,
SIES Graduate School of Technology

## Slide 2
Book :
David Hanes, Gonzalo Salgueiro, Patrick Grossetete, Robert Barton, Jerome Henry, IoT Fundamentals Networking Technologies, Protocols, and Use Cases for the Internet of Things CISCO , Ch 4 ,5
Analytics for the Internet of Things (IoT) Intelligent Analytics for Your Intelligent Devices.Andrew Minteer,Packet , ch 2
Blooms level : L1,L2,L3,L4

## Slide 9
JNIT

## Slide 24: Introduction
The RFID system consists of a tag (also known as a transponder) attached to the object being identified
– integrated circuit and an antenna.
Reader-queries the tag using radio frequency (RF) waves, and gets the identity of the tag via the RF waves.
The RFID systems operate in various frequency bands.

## Slide 25: Introduction
Some of the most popular frequencies are:
– 125 kHz to 134.2 kHz (LF: low frequency);
– 13.56 MHz (HF: high frequency);
– 860 to 915 MHz (UHF: ultra-high frequency); and
– 2.45 GHz to 5.8 GHz (microwave frequency).

## Slide 26: Introduction
The RFID systems operating in the LF band were the first to be deployed in the market for high- volume short-range industrial applications and car immobilizer devices.
These systems are attractive in systems where the
data rates are not very high.

## Slide 27: Introduction
The HF RFID systems are capable of handling much higher data rates compared to the LF system,
– and the tag antenna is much smaller.
HF systems have longer read range compared to the LF systems.
The UHF RFID system has a much longer read range and much higher data rate compared to the LF and HF systems.
However, the UHF system does not work very well in the presence of metallic objects, water and the human body, compared to the LF system.

## Slide 28: Some RFID readers
Source: www.b1u3yrfid.org

## Slide 29: RFID tag memory
15
•
•
•
Read-only tags
Tag ID is assigned at the factory during manufacturing
  Can never be changed
  No additional data can be assigned to the tag Write once, read many (WORM) tags
Data written once, e.g., during packing or manufacturing
  Tag is locked once data is written
  Similar to a compact disc or DVD Read/Write
Tag data can be changed over time
  Part or all of the data section can be locked

## Slide 30: RFID readers
16
•
•
•
Reader functions:
Remotely power tags
Establish a bidirectional data link
Inventory tags, filter results
Communicate with networked server(s)
Can read 100-300 tags per second
Readers (interrogators) can be at a fixed point such as
Entrance/exit
Point of sale
Readers can also be mobile/hand-held

## Slide 31: RFID application points
17
♣ Shipping Portals
Assembly Line
♣ Handheld Applications

## Slide 32: RFID applications
18
•
•
•
•
Manufacturing and Processing
Inventory and production process monitoring
Warehouse order fulfillment
Supply Chain Management
Inventory tracking systems
Logistics management
Retail
Inventory control and customer insight
Auto checkout with reverse logistics
Security
  Access control
  Counterfeiting and Theft control/prevention
Location Tracking
  Traffic movement control and parking management
  Wildlife/Livestock monitoring and tracking

## Slide 33: Smart groceries
19
•
Add an RFID tag to all items in the grocery.
•
As the cart leaves the store, it passes through an RFID transceiver.
•
The cart is rung up in seconds.

## Slide 34: Smart cabinet
1. Tagged item is removed from or placed in “Smart Cabinet”
4. Designated individuals are notified regarding items that need attention (cabinet and shelf location, action required)
“Smart Cabinet” periodically interrogates to assess inventory
Server/Database is updated to reflect item’s disposition
Passive read/write tags affixed to caps of containers
Reader antennas placed under each shelf

## Slide 35: Smart fridge
Recognizes what’s been put in it
Recognizes when things are removed
Creates automatic shopping lists
Notifies you when things are past their expiration
Shows you the recipes that most closely match what is available
21

## Slide 36: Smart groceries enhanced
•
Track products through their entire lifetime.
Source: How S22tuff Works

## Slide 37: Some more smart applications
23
•
•
•
•
“Smart” appliances:
Closets that advice on style depending on clothes available.
Ovens that know recipes to cook pre-packaged food.
“Smart” products:
Clothing, appliances, CDs, etc. tagged for store returns.
“Smart” paper:
Airline tickets that indicate your location in the airport.
“Smart” currency:
Anti-counterfeiting and tracking.
•
“Smart” people ??

## Slide 41: Principle of RFID
https://www.youtube.com/watch?v=Ukfpq71BoMo
Consider a coil made of copper wire through which
alternating current is flowing.
The coil offers impedance to the source and a voltage develops across its terminals.
It is possible to increase the voltage by connecting a capacitor in parallel with the coil.
“primary” coil

## Slide 42: Principle of RFID
Another coil-“secondary” coil,
Close to the first.
Due to electromagnetic induction, voltage appears across the terminals of the secondary coil.
The amplitude of the voltage depends on the size, shape, location and orientation of the secondary coil.
If we connect a resistor (also known as a load) across the terminals of the secondary coil, current flows through it.

## Slide 43: Principle of RFID
The primary coil can be thought of as the reader of the RFID system, and the secondary coil as the transponder or tag.
The tag can convey any message back to the reader using RF signals, by simply changing the load connected to its terminals.
This could be achieved by switching in a load to represent a logical state 1 and taking off the load to represent a logical state 0.

## Slide 44: Antenna fields: Inductive coupling
Transceiver
Tag Reader
antenna
RFID
Tag
IC or microprocessor
antenna

## Slide 45: Antenna fields: Propagation coupling
Transceiver
Tag Reader
antenna
RFID
Tag
IC or microprocessor
antenna

## Slide 46: RFID Middleware
A typical RFID system can have
  several readers and tags (operating in different frequency bands and using various protocols),and
  several applications accessing these tags via the readers.
It is important to provide a seamless connectivity between the RFID hardware and the application by insulating the applications from the RFID hardware.

## Slide 47: RFID middleware
is comprised of
General middleware architecture three components
– device interface;
– core processing interface;
– application interface

## Slide 49: Issues
An RFID system has a high reliability when operating under controlled conditions.
  a reader trying to read a tag
  As long as the tag is within a specific distance of the reader antenna
In a practical scenario,
  the tag is attached to an object whose electrical properties are different to that of free space.
  This generally degrades the performance of the tag (in exceptional circumstances it can enhance the performance).

## Slide 50: Issues
Several tags try to communicate with the reader and several readers trying to read several tags at the same time.
  This results in a collision of data being transferred between the readers and tags.
  Algorithms to avoid collisions have been proposed and successfully used to solve some of these issues.

## Slide 51: Issues
Several tags in the vicinity of the reader,
  Tags has a unique serial number.
  If the reader issues a command asking the tags to respond back with their serial numbers
  All the tags receiving this command will respond back with their respective serial numbers, causing collision.

## Slide 52: Issues
The reader can perform read and write operations
on the selected tag.
If there is a collision, the reader issues another request command by lowering the value of the parameter, thereby targeting a smaller group of tags to respond.

## Slide 53: Issues
Propagation of electromagnetic waves is influenced by the environment.
Therefore, the amount of energy reaching the tag antenna depends on the interaction of the waves and the environment in which the reader and the tag are placed.

## Slide 54: Issues
The transmission power of the reader is increased in steps of 0.1 dB and an attempt is made to read the tag.
The lowest transmission power at which a tag is read, which is known as the “threshold power”, is recorded.
Threshold power is the smallest transmission power required to detect (read) the tag with all other parameters held constant.
It is also possible to measure the threshold power for
writing data into a tag.
– less challenging.

## Slide 55: Issues
Privacy of data stored in the tag becomes an issue when these are associated with people.
For example, in the retail sector,
– it is possible to link the product (via the data stored in the tag attached to it) and the person buying it (through his or her credit card number).
If a tag can be associated with a person (via a tag stuck on the shirt that the person is wearing), the RFID system using a collection of stationary readers could be used to track the person’s movement.

## Slide 56: Issues
Security of information stored on the tag also plays a crucial role in several applications.
  Issues such as tampering with the data stored in the tag,
  altering the association between the tag and the product,
Collecting security-related data stored on the tags, etc. have prompted designers to implement encryption techniques to secure the information on the tag itself.

## Slide 57: NFC (Near Field Communication)

## Slide 76: Indoor Positioning System
Real Time Locating Systems (RTLS)

## Slide 77
Real Time Locating Systems (RTLS) provide knowledge by delivering precise visibility of critical assets, supply chain, manufacturing, and human, in real-time.
For transportation and logistics enterprises, this knowledge means having end-to-end visibility and Traceability of all Containers, pallets, and packages.
For manufacturers, it enables intelligent management and flow of all critical assets, whether in the facility or at a sprawling storage yard.

## Slide 78
Under security and safety operations, it means controlling employee access and ensuring they do not linger in hazardous areas beyond safety requirements.
RTLS or indoor positioning systems (IPS) can be simply described as GPS on steroids but used indoors for the purpose of Tracking, locating and monitoring the activity of people and things.

## Slide 79
It is used in healthcare, manufacturing, smart warehouses, hospitality, education, and other industries for the purpose of maximizing workflow efficiency, safety, wayfinding, and inventory and asset control and has been proven to deliver significant return on investment (ROI).