## Slide 1: IoT Protocols https://www.youtube.com/watch?v=l-oY-ePIdRs https://www.youtube.com/watch?v=QXV_HgGO--g https://www.youtube.com/watch?v=NSkIHdV6NoY

## Slide 2: Bluetooth, Zigbee, WiFi

## Slide 16
Zigbee

## Slide 17: ZigBee
IEEE 802.15.4-based specification for a suite of high-level communication protocols
Used to create personal area networks with small, low-power digital radios
ZigBee based applications
  Home Automation
  Medical Device Data Collection
  other low-power low-bandwidth

## Slide 34: WI FI

## Slide 46
Common Radio Protocols
Design requirements
  Short range
  High data rate
  Small number of devices
Common protocols
  Bluetooth/Low Energy
  ZigBee
  Ant
  WiFi
Radios for indoor applications
Radios for outdoor IoT applications
Design requirements
  Long range
  Low data rate
  Large number of devices
  Low energy consumption
Common protocols
  GSM/GPRS
  LTE (Long term Evolution)
Emerging protocols
  Sigfox/LoRA (Long Range)
  Narrow band LTE
  Backscatter
Notes: https://www.sparkfun.com/products/10268
http://www.directindustry.com/prod/digi-international/zigbee-radio-modules-16022-799537.html
http://labs.beatcraft.com/en/index.php?gadget%20%2F%20ANT%20module
https://www.sparkfun.com/products/10822

## Slide 47
Radio band: 2.4-2.48 GHz
Average 1 Mbps - Up to 3 Mbps
Supports point-to-point and point-to-multipoint
  Creates personal area networks (PANs/Piconets)
  Connects up to 8 devices simultaneously
Minimal interference between devices
  Devices alter frequencies arbitrarily after packet exchanges -up to 1600 times/second - frequency hopping
3 classes of Bluetooth transmit power
Bluetooth
Notes: http://electronics.howstuffworks.com/bluetooth.htm
http://www.mobileinfo.com/Bluetooth/applic.htm
http://bluetoothinsight.blogspot.com/2008/01/bluetooth-power-classes.html

## Slide 48
Wireless communication between devices
  Mobile phones, laptops, cameras, gaming controllers, computer peripherals, etc
Short range sensor transmission
Share multimedia - pictures, video, music
A2DP - Advanced Audio Distribution Profile
  Stream audio wirelessly
Bluetooth Applications
Notes: http://www.bluetooth.com/Pages/Bluetooth-Home.aspx

## Slide 49: Bluetooth low energy
  From 2001 – 2006 Nokia asked:
  How do we design a radio that can transmit short bursts of data for months or years only being powered by a coin cell battery?
  The answer is: Keep the radio asleep mode most of the time!
  Advertise on only one of three channels
  Transmit quickly at 1 Mbit/s
  Make the minimum time to send data only 3 msec
  Make a very predictable time when the device accepts connections
  Limit the max transmit power to 10 mW
  However, don’t sacrifice security: AES 128-bit

## Slide 50
Zigbee is built on top of 802.15.4
Radio bands: 868MHz in Europe, 915MHz in US and Australia. 2.4GHz else worldwide.
Low data-rate - 250 kbps, low power – Up to 1000 days
Transmits over longer distances through mesh networks
Zigbee/802.15.4

## Slide 51: Why ZigBee?
Low Power, Cost, and Size
Straightforward configuration
Good support and documentation
  Lots of products already on the market
Mesh Networking
Lends itself well to many different applications
Very low wakeup time
  30mS (Zigbee) vs. up to 3S (Bluetooth)

## Slide 52
Wireless environmental sensors
  Temperature, pressure, sound, luminous intensity
Medical devices
  Glucose meters, heart monitors
Household automation
  Security/temperature controllers
  Smoke/motion detectors
Zigbee/802.15.4 Applications

## Slide 53
6LoWPAN stands for IPv6 over Low-power Wireless Personal Area Networks.
It is a standard protocol for realizing IPv6 communication on wireless networks composed of low-power wireless modules.
6LoWPAN specification contains packet compression and other optimization mechanisms to enable the efficient transmission of IPv6 packets on a network with limited power resources and reliability, which makes efficient IPv6 communication over low-power wireless networks possible.
6LowPAN
Notes: http://compnetworking.about.com/od/wirelessfaqs/f/5ghz-gear.htm
http://compnetworking.about.com/cs/wireless80211/a/aa80211standard.htm
2.4GHz band, cheaper, a little lower speed
5GHz band, expensive but better performance due to less interference

## Slide 54
Various low-power wireless networks have been proposed and implemented before 6LoWPAN, but currently, 6LoWPAN is regarded as one of the preferred protocols to realize the Internet of Things (IoT).
This is because 6LoWPAN communication based on IPv6 allows once closed low-power wireless networks to interface with the global network, the Internet, and implement more advanced intelligent services that were not possible in the past.
6LowPAN
Notes: http://compnetworking.about.com/od/wirelessfaqs/f/5ghz-gear.htm
http://compnetworking.about.com/cs/wireless80211/a/aa80211standard.htm
2.4GHz band, cheaper, a little lower speed
5GHz band, expensive but better performance due to less interference

## Slide 55
Let us take the future smart house architecture.
Optimized control of a smart house requires the information to be collected from various sensors. The control system consolidates the information to recognize the real-world context then gives appropriate optimized feedback to the real-world environment using actuators.
Management of a smart house by executing control logic on the reliable cloud server infrastructure is cost-effective from the viewpoint of high scalability, usability, and low maintenance cost. To realize such a control framework, 6LoWPAN‘s conformance to the Internet protocol plays an important role.
6LowPAN
Notes: http://compnetworking.about.com/od/wirelessfaqs/f/5ghz-gear.htm
http://compnetworking.about.com/cs/wireless80211/a/aa80211standard.htm
2.4GHz band, cheaper, a little lower speed
5GHz band, expensive but better performance due to less interference

## Slide 56
Notes: http://www.atmel.com/microsite/AT86RF232/default.aspx

## Slide 57
 | Bluetooth | Zigbee/802.15.4 | WiFi
Speed | Moderate | Low | High
Range | Moderate - High | High | High
Power Consumption | Low - Moderate | Low | High
Protocol Comparisons